## Slide 1
BUFR Meta Data
C. Marquardt
EUMETSAT
20 March 2024

## Slide 2: Agenda
Time and geolocation
Already addressed in the new BUFR proposal.
Product Confidence Flags
Some are dubious IMHO.
Levels
Proposing a recommendation.

## Slide 3: Time and geolocation
Same as already proposed in Harald’s IROWG-4 Summary paper from 2015:
  Occultation reference time shall be “nominal reporting time” as used for georeferencing the occultation, ideally for SLTA = 0
    Old BUFR template: Time significance (0 08 021): 25, TimeIncrement = 0
  Provide antenna positions
  Satellite and occultation positions in Earth Fixed coordinates
  Satellite velocities (3 04 031) as absolute velocities (i.e. as quantity in an inertial system). Components to be given in Earth Fixed coordinates
  Azimuth (0 05 021) clockwise against North, 0° - 360°
Taken care of in new BUFR template proposal already as a reference time is explicitly requested. Start and end of occultations are provided as time increments.

## Slide 4: Product Confidence Flags (PCDs – Second Table 9)
Descriptor | Bit | Meaning when clear | Meaning when set
0 33 039 | 1 | Nominal quality | Non-nominal quality
 | 2 | NRT product | Offline Product
 | 3 | Descending occultation | Ascending occultation
 | 4 | Excess phase processing nominal | …non-nominal
 | 5 | Bending angle processing nominal | …non-nominal
 | 6 | Refractivity processing nominal | …non-nominal
 | 7 | Meteorological processing nominal | …non-nominal
 | 8 | Closed-loop data only used | Open-loop data included
 | 9 | No surface reflections detected | Surface detections detected
 | 10 | L2P GNSS signals used | L2C GNSS signals used
 | 11-13 | Reserved | 
 | 14 | Background profile nominal | …non-nominal
 | 15 | Retrieved profile | Background profile
 | All 16 | As above | Missing

## Slide 5: Dubious components of the current PCD
Open- vs closed-loop
  Today, all active receivers offer open-loop data in the troposphere; some do not even have closed data anymore (TrIG, Spire, PlanetIQ)
  I would drop this, or add a ternary option – closed-loop only, closed-& open-loop, open-loop only – plus another descriptor identifying the height of the transition between open- and closed-loop.
Surface reflections
  We once thought the presence of surface reflections might degrade data quality; the opposite seems to be true.
  I don’t know of any processing centre providing a surface reflection flag.
  I would drop this.
L2/P vs L2C
  Today’s multi-GNSS receivers provide measurements from a mixture of signal types.
  I would prefer to record the actual signal types for each frequency, e.g. as an IGS Rinex observation code (section 5.2.17 in the RINEX specification).

## Slide 6: Levels
Harald’s discussion summary from 2014 recommends a set of fixed levels.
  I would adopt this as a recommendation (but not as mandatory), further recommending
  That level values are fixed, not only their number;
  How refractivity levels relate to impact parameters.